## Slide 1: Introduction to Computer Science and Engineering from a programming language viewpoint
Isao Sasano
2020 October 2, 9:00-10:40
Department of Computer Science and Engineering

## Slide 2: Self Introduction
Isao Sasano, Professor, Department of Computer Science and Engineering, College of Engineering, Shibaura Institute of Technology.
Ph.D. (March 2002, University of Tokyo) (The thesis is about program transformations.)
My current research is in programming languages (in particular, tools for programming support).
Self introduction
I introduce computer science from the view point of programming languages.

## Slide 3: Analog computers
Compute by using physical phenomena
  Sundial --- a device that tells the time of day (B.C. 3500, Egypt)
  Slide rule (slipstick) --- a mechanical analog computer to calculate multiplication, division, exponents, roots, logarithms and trigonometry, but not for addition or subtraction (17th century, UK)
  Differential analyzer --- a mechanical device to integrate differential equations (19th century, France)
  Various other analog computers to calculate various things.
Computation is not so slow but not so accurate.
What is computed has to be designed beforehand.
Nowadays analog computers are not so used and researched.

## Slide 4: Mechanical digital computer (for polynomials)
A mechanical calculator designed to tabulate polynomial functions. Various functions including logarithmic or trigonometric ones can be approximated by polynomials.
It could be used for making many useful tables, although Babbage failed to physically construct the difference engine.
Difference engine developed by Charles Babbage, 1791-1871, UK.

## Slide 5: A general purpose digital computer
Vacuum tube 17,000, 150kW, 167m2.
Used for making tables for firing angles of bombs.
ENIAC,
University of Pennsylvania, US, 1946.

## Slide 6: Encoding
(ex) number 1
  1 (00000001, a binary number, 1 byte)
Character ‘a’
  97 (01100001, a binary number, 1 byte)
String “ab”
  97 98 0 (01100001 01100010 00000000, three binary numbers, 3 byte. Suppose 0 represents the end of string.)
There are various character encoding (correspondence between characters and numbers). Unicode, Shift-JIS, etc. are often used in Japan.
When processing information on digital computers, we have to express the information by a sequence of symbols (typically 0 and 1, so binary numbers). This is referred to as encoding. Although ENIAC uses decimal numbers, modern computers use binary numbers.

## Slide 7: Images
encode
decode
Divide an image into cells (discretization) and then express the color of each cell by the ratio in a natural number of red, green, and blue (quantization).
255 255 255 | 255 255 255 | 255 255 0 | 255 255 255 | 255 255 255
255 255 255 | 0 0 255 | 0 0 255 | 0 0 255 | 255 255 255
0 255 0 | 0 255 0 | 0 255 0 | 0 255 0 | 0 255 0
An image
Discretize and quantize
For instance, 24 bit BMP expresses each color by a number 0-255. There are various other encoding. JPEG decomposes an image by frequency and reduces the information of frequencies that human beings may not recognize.

## Slide 8
Sounds
There are various sound encodings. For instance, MP3 decomposes sounds into basic waves of various frequencies and then reduces the information of some frequencies that human beings may not recognize.
Express amplitude at fixed intervals by integers (by discretization and quantization).
Time
Amplitude

## Slide 9: Principles of information processing in digital computers
Express the information (numbers, characters, images, sounds, etc.) by a sequence of symbols (typically 0 and 1) (encoding).
  A sequence of symbols corresponds to a natural number, so this is to express the information in a number. Structures (like trees) can be expressed by a number which corresponds to locations in memory.
Process the information by a program. (Do some computation.)
In digital computers, we can do any (computable) computation (information processing) by writing some suitable program. In contrast, in analog computers, we have to make a device for a computation.
Alan Turing, “On Computable Numbers, with an Application to the Entscheidungsproblem”. Proceedings of the London Mathematical Society, Ser. 2, Vol. 42: pp. 230–265. 1937.
In 1940s, von Neumann read the paper by Turing and then invented von Neumann architecture (stored-program computers).

## Slide 10: Benefits of expressing information by a sequence of symbols
We can store, restore, copy of information accurately and fast.
  Instead, some information are lost by discretization and quantization.
  By increasing the amount of data, we can increase accuracy.
We can process the information accurately and fast by writing a program.

## Slide 11: Inside the digital computers
0
1
1
0
0
1
1
0
1
1
1
1
Digital computers interpret some physical phenomena by two states: CPU voltage --- high or low, hard-disk of ferromagnet --- N and S, hard-disk of ferroelectric --- + and -, CD-ROM --- concavo-convex. These states (informations) are communicated with HDD, keyboard, display, and so on.

## Slide 12: Digitalization
We can interpret the value as 1 or 0 whether or not the value exceeds some threshold. This is digitalization.
0
1
1
1
0
Voltage in CPU and concavo-convex in CD-ROM are physical phenomena or material. These values/shapes change continuously and not digitalized like 0 and 1.

## Slide 13: What are digital computers?
What are digital computers?
  Machines for computation by using finitely many kinds of symbols (typically 0 and 1).
What is computation?
  It was difficult to define what is computation. In 1930’s, it was one of the problems considered by mathematicians.
What are digital computers?

## Slide 14: Origin of computer science
Kurt Gödel : 1906-1978, logician in Czech Republic
Alonzo Church : 1903-1995、logician in US
Alan Turing : 1912-1954, mathematician in UK
“What are computable functions” was a question in 1930’s.
(1) partial recursive function, Kurt Gödel
(2) lambda calculus, Alonzo Church
(3) Turing machine (TM), Alan Turing
It was proved that these three are equivalent w.r.t. the computational power.
Nowadays it is consensus that these three are the definition of computable functions.

## Slide 15: Turing machine
Controller
Controller reads the symbol pointed by the header and rewrite the symbol and move to the left or to the right following a rule for the state and the symbol. If there are no such rule, the machine stops.
Controller can take finitely many states.
Rewrite symbols which consist of finitely many kinds of symbols on the tape.
(corresponding to CPU)
A tape of infinite length (corresponding to memory)

## Slide 16: What Turing machines can do
Input: Symbols on the tape when TM starts
Output: Symbols on the tape when TM stops
Examples of computable numbers:
π 3.1415926535….
e 2.718281828…..
Intuitively, numbers for which some algorithm exists are computable.
The set of real numbers that are computable is countably infinite, because the controller and the tape can take countably infinite states.

## Slide 17: Universal Turing machine (1)
Each TM is a computer that does some specified computation.
TM that computes π
TM that computes e
…
We’d like to compute them in one machine.
Universal TM

## Slide 18: Universal Turing machine (2)
A universal TM is one that simulates any TM.
Initial symbols on the tape:
Rules of the TM we simulate (encoded by some sequence of symbols)
Digital computers have computational power equivalent to a universal TM.
By writing a suitable program, we can simulate any digital computer.
(This implies that all the digital computers are equivalent w.r.t. the computational power. )

## Slide 19: Universal Turing machine (3)
We can do any (computable) computation by giving sequence of symbols, which encodes some TM, on the initial tape on a universal TM.
John von Neumann considered von Neumann architecture (or stored-program computer) influenced by the paper by Alan Turing.

## Slide 20: Principles of information processing on digital computers (again)
(1) Represent the information to process by a sequence of symbols taken from a finite set of symbols (not necessarily 0 and 1).
(2) Process the sequence by a program (which is also a sequence of symbols).
(Cf.) Godel numbers --- all the logical expressions can be expressed by natural numbers (which was used for proving the incompleteness theorem).
Nowadays this idea is used not only for logical expressions.

## Slide 21: What Turing machines cannot do
There does not exist a TM that judges whether or not some Turing machine halts with some tape.
There does not exist a C program that judges whether or not some given C program halts.
A typical example that actual digital computers cannot do

## Slide 22: (Cf.) Halting problem and compilers
i=1;
while (i != 0) i = 2;
printf (“%d”, i);
Some people may consider it is convenient if compilers show warnings if the program contains while loops of the above kind.
This is impossible in general, so compilers do not (cannot) provide such functionality.
(If a compiler could judge whether or not any given while loop halts, we have solved the halting problem.)
This segment of C program does not halt forever.

## Slide 23: Programming languages
We say a programming language is Turing complete if it can describe any Turing machine. Usual programming languages (such as C, Java, Ruby, and so on) are Turing complete. Usual programming languages are equivalent w.r.t. description power.

## Slide 24: Programming languages
There are various kinds of programming languages. We use some suitable language for each application.
Machine language
Assembly language
Fortran
Lisp
Pascal
C
ML
Java
….
Programming languages are read and written by more than one people. Compilers may be implemented by a person other than language designer. So the semantics of programs should be specified.

## Slide 25: Syntax and semantics
A programming language can be defined by defining its syntax and semantics.
Consider how to represent a number.
325
By writing 3, 2, 5 next to each other, we can express a number 325 (three hundred and twenty five).
0
1
2
3
4
5
6
7
8
9
325
325
Alphabets
Language
Semantics
denote
arrange in line
(numerals)
(sequences of numerals)
(natural numbers)

## Slide 26: Syntax and semantics
Syntax description (sequence of numerals)
We would like to define a set of sequences of numerals.
<numeral> ::= 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Definition of sequences of numerals
We cannot enumerate all the sequences, since there are infinitely many ones.
We would like to express an infinite set by a description of finite length.
--- We use the idea of grammars.
Definition of numerals

## Slide 27: Syntax and semantics
<numeral> ::= 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
<seq> ::= <numeral> | <seq> <numeral>
A numeral is 0 or 1 or 2 or … or 9.
A sequence is a numeral or a sequence followed by a numeral.
Mathematically, we use the inductive definition of a set.

## Slide 28: Syntax and semantics
Semantics of a numeral
0
1
2
3
4
5
6
7
8
9
(numerals)
(natural numbers)
0
1
2
3
4
5
6
7
8
9
digval
digval (0) = 0
digval (1) = 1
...
digval (9) = 9
10
11
12
…

## Slide 29: Syntax and semantics
Semantics of sequences of numerals
325
(sequences)
numval
(natural numbers)
0
1
2
3
4
5
6
7
8
9
10
11
12
…
325
…
numval (d) = digval (d)
numval (nd) = numval (n) * 10 + digval (d)
The function numval is defined inductively (or recursively).
(ex) numval (325) = numval (32) * 10 + digval (5)
= (numval (3) * 10 + digval (2)) * 10 + digval (5)
= (3 * 10 + 2) * 10 + 5
= 325
…

## Slide 30: Syntax and semantics
Semantics of a programming language (in the case of simple imperative language)
begin
fac := 1;
while n > 0 do
begin fac := fac * n; n := n -1 end
end
(programs)
(Partial functions from states to states)
[A program]
s
The function that maps the value of the variable fac to the factorial of the value of the variable n.
s

## Slide 31: Syntax and semantics
Like the definition of semantics of sequences, to define the semantics of a program from the semantics of sub-programs is called denotational semantics. It was developed by Dana Scott. We use this when we argue formally the semantics of programming languages.
There are two more formal semantics: operational semantics and axiomatic semantics.
Usually, semantics of languages are specified by using natural languages like English, Japanese, Indonesian, and so on. But it does not suit formal argument.

## Slide 32: Any questions?

## Slide 33: Research topics
Theory and implementation of programming support
  Identifier completion, syntax completion
  code clone detection for functional programming languages
Theory and implementation of programming learning support
  Eliminating goto statements for C (replacing with, e.g., while, break, and continue statements)
  Visualizing pointers in C programs

## Slide 34
Uses LR parser
Generates syntax completion functionality from LR grammar description
Presented at PEPM 2020
Syntax completion

## Slide 35
Syntax completion

## Slide 36
Syntax completion

## Slide 37
Identifier completion for (a subset of) Standard ML
Filtering identifiers by using context such as typing information and scopes
Published in Higher Order and Symbolic Computation 25(1), 2013
Source code is available at http://www.cs.ise.shibaura-it.ac.jp/lambda-mode/
Identifier completion

## Slide 38: An example
reducing typing errors

## Slide 39
Identifier completion allowing syntax errors
  Programs may be written in any order
  There may be some syntax errors in the program text
Utilizing Error recovery functionality in Yacc
Presented at MPSE2014
Source code is available at http://www.cs.ise.shibaura-it.ac.jp/mpse2014/
An extension

## Slide 40
Detecting code clones in functional programming languages taking into account the gaps by function applications
Presented at PEPM2017
Detecting code clones

## Slide 41
Eliminating goto statements in C programs
  Transforming programs containing goto statements into ones without goto statements
Programming learning support

## Slide 42
Generating C programs by slightly changing a given C program
Programming learning support